## Slide 1
Automated Hyperspectral Pyrometry of Floating Zone Growths
Naman Parikh1, David Elbert2, Tyrel McQueen3
1Department of Physics, Carnegie Mellon University
2Hopkins Extreme Materials Institute
3Department of Chemistry, Johns Hopkins University

## Slide 2
Laser Diode Floating Zone

## Slide 3
Scott S. Dossa, Jeffrey J. Derby
https://doi.org/10.1016/j.jcrysgro.2022.126723

## Slide 6
Physical
Digital
Data
?
Scott S. Dossa, Jeffrey J. Derby
https://doi.org/10.1016/j.jcrysgro.2022.126723
Notes: So, what are these 3 elements for floating zone growths? The physical aspect would be the growth itself, the process of the growth and the underlying physics that governs the growth. Also an important part of the physical element is the controls of the furnace. The experimenter can change things like the rotation speed and pull rate, and these affect the growth. The last physical element is the crystal the is made at the end. Whether it’s a single or multiple crystal, it’s structure, and it’s properties. The digital twin that is being made in other work is computational models and simulations of the growths. This includes finite element models to track the thermal distribution and fluid flow during a growth. Currently, these models have had some success in different ways of simulating the molten zone and solid-liquid interface, but they are informed only by physics theory and not actual growth data, and they are not validated against physical growths. So, they are fundamentally disconnected because of the lack of data.

## Slide 7
7
Scott S. Dossa, Jeffrey J. Derby
https://doi.org/10.1016/j.jcrysgro.2022.126723
Modeling – NaNO3
Notes: What makes these models difficult to use because the inputs for the models are not the same as the inputs for a physical growth. For a physical growth, we have things like the laser power and pull rate, but the input for the models is things like the temperature field, which we don’t know how to measure for a physical growth. IF I WANT TO USE THE MODEL TO INFORM MY GROWTH, I need some way to measure the temperature distribution so I can then input it into the model. Additionally, the model doesn’t know how to determine how the heat will flow as the samples are heated up during the growth. Temperature is missing as data for the physical growths and because of this is missing from the model’s ability to predict. So, data that would be useful in developing a digital twin is the temperature distributions of growths.

## Slide 8
8
Scott S. Dossa, Jeffrey J. Derby
https://doi.org/10.1016/j.jcrysgro.2022.126723
Modeling – NaNO3

## Slide 9
Digital Twins
“Set of virtual information constructs that mimics the … system”
“Has a predictive capability”
“Informs decisions that realize value”
“Dynamically updated with data from it’s physical twin”
National Academies of Sciences, Engineering, and Medicine
https://doi.org/10.17226/26894

## Slide 10
Digital Twins
“Set of virtual information constructs that mimics the … system”
“Has a predictive capability”
“Dynamically updated with data from it’s physical twin”
National Academies of Sciences, Engineering, and Medicine
https://doi.org/10.17226/26894

## Slide 11
Research Question
How can we collect temperature data from lab growths?

## Slide 12
Hyperspectral Camera

## Slide 13
What are the steps?
Collect data
Analyze the data

## Slide 16
Analysis
Blackbody

## Slide 17
Least Squares Regression
Model Function
Parameters
Guess Parameters
Minimize Residuals

## Slide 18
Blackbody Model Function
Emissivity
Parameters
Stray Light Offset

## Slide 19
Run the Regression
Data
Fitted with T=1298 K
Full Spectrum

## Slide 20
Into the furnace
20
Kelvin

## Slide 21
What’s next?
Optimizing the analysis
Collect tons of data
Validate and inform models
Notes: Optimizations include performance improvement and potentially needing to reduce sensitivity to atomic emission spikes

## Slide 22
Physical
Digital
Data
Autonomous Experimentation

## Slide 23
Physical
Digital
Data
Measurement
Model validation and updating
Predictions
Promising growths

## Slide 24
Physical
Digital
Data
“Dynamically updated with data from it’s physical twin”
“Bidirectional interaction”
“Informs decisions that provide value”

## Slide 25
Evan Crites (McQueen Lab, PARADIM)
Maggie Eminizer (IDIES)
NSF Awards #2039380 (PARADIM) and #2129051 (VariMat)
Acknowledgements
Physical
Digital
Data

## Slide 26
Extra Slides – Other Carbon Rod Spectra

## Slide 27
Carbon Rod Corrected

## Slide 28
Carbon Rod Uncorrected

## Slide 29
Notch Filter Dip

## Slide 30
Laser Light Spike

## Slide 31
Extra Slides – Camera Motion

## Slide 32
Notes: How do we make it scan?

## Slide 33
Notes: Why does it need to move?
Important to note that the computer syncs the start of the image capture and the movement of the stage

## Slide 35
Notes: How do we sync the motor with the image capture? We are replacing the stage with the motor

## Slide 36
Extra Slides – Streaming

## Slide 38
Notes: Animate in one piece at a time